## Slide 1: CIS 4930-001: Introduction to Augmented and Virtual Reality
Graphics Pipeline

## Slide 2
A Simplified View of the Graphics Pipeline
http://romain.vergne.free.fr/teaching/IS/SI03-pipeline.html

## Slide 3
Full OpenGL 4.4 Pipeline
http://openglinsights.com/pipeline.html

## Slide 4
The ”real” Virtual Reality
  What does it take to create a virtual world indistinguishable from the real, in the visual sense?
    80 million polygons/frame is threshold of “reality”, a sufficiently rich approximation that audiences cease to be concerned about its authenticity.
      Prediction from Alvy Ray Smith, (Microsoft Graphics Guru) Co-founder of Pixar
    80M ppf * 60 fps = 4.8 Gpolygons/second
  Nvidia GeForce Titan RTX
    Conventional: 170 Gpixels/second
    Ray-tracing: 11 Brays/second
    4K Resolution: 3840x2160=8.3Million pixels
  So, we’re approaching/surpassing the reality threshold

## Slide 5
Real time ”A Bugs Life”
  1998 Pixar/Walt Disney released A Bugs Life.
  Generating an average frame took 3-4 h (even up to 20h) on a 330Mhz UltraSPARC
  For a minimum frame rate of 12 fps would take a speed-up of 150,000 times
  Given Moore’s law, (acceleration rate of 2 times every 18 months)
    would get us to year 2024.
  Graphic chips have developed faster than that
  Graphic chipsets doubling every 6 months
    Would lead to 2007

## Slide 6
Real time bugs life – Unreal Engine
https://youtu.be/qlyzo9ll9Vw

## Slide 7
Real Time ”A Bugs Life”
  Very unlikely trend can continue
    Electron leakage and Quantum effects will appear when the electronics is shrink far enough. (Colin P. Williams et. al., Explorations in Quantum Computing)
  Methods for optimizing the graphics, both in software and later in hardware helped with performance and realism leaps

## Slide 8
Real Time Graphics
  James Helman in “Architecture and Performance of Entertainment systems” SIGGRAPH-94 noticed that
    If frame rate is lower than display refresh rate (e.g., 60Hz), motions are experienced unnatural
    Ideally we would like to have frame rate == display refresh rate (generally 60Hz)

## Slide 9
Frame rate - so very important for VR
  Low frame rate:
    Latency for the user
    No presence
  Uneven frame rate
    Due to different object detail in the scene
    Jerky graphics
    Hard to interact with objects when speed in unpredictable
  Constant high frame rate – What we wish for
    6 fps, a sense of interactivity
    15 fps is real time
    30-60 minimum target for games
    > 72 fps changes in display rate is undetectable

## Slide 10
Why is high frame rate hard: Example
  Display
    1280 x 1024; 24 bit (rgb); 32 bit (depth)
    30 Hz update rate
  Scene
    100,000 triangles
    Ambient and diffuse illumination

## Slide 11
Per-Frame Geometry Calculations
  Geometry Traversal
    300,000 vertices, normals (6 FP load/store)
    100,000 start/end tokens, (2 integer load/store)
    2M loads/stores per frame
  Modeling transformation
    300,000 vertices, normals (25 mults + 18 adds)
    7.5M mults, 5.4M adds per frame
  Trivial accept/reject (gross clipping)
    Dot each vertex against six planes
    24 mults + 18 adds per vertex: 7.4M mults, 5.4M adds per frame

## Slide 12
Per-Frame Geometry Calculations
  Lighting
    12 mults + 5 adds per vertex: 3.6M mults, 1.5M adds per frame
  Viewing transformation
    8 mults + 6 adds per vertex: 2.4M mults and 1.8M adds
  Clipping
    Highly variable
    Division by w (assuming all primitives within view frustum)
      3 divs per vertex, 0.9M divides
  Transform to NDC
    2 mults + 2 adds per vertex: 0.6M mults, 0.6M adds

## Slide 13
Per-Frame Geometry Calculations
  Total for geometry:
    30+ million loads & stores (depending on dataflow)
    22M mults/divides + 15M adds per frame
At 30Hz frame rate, more than TWO GigaFlops!
(Not including application, system overhead, rasterization, etc.)
Modern intel chips do up to 32 flops per cycle

## Slide 14
Measuring performance
  Common Measurements
    GFLOPS
    Pixels per second (GP/s)
    Texels per second (GT/s)
    Memory bandwidth (GB/s)
  H/W manufacturers present peak rates
    Close to impossible to reach
  Real world tests
    Most tests are based on games: Quake, Unreal, etc…
    Measures the throughput of the whole system

## Slide 15
Why hardware?
  Why special purpose hardware for graphics?
    Even transmitting the geometry over the bus takes time
    Example:
      Triangle requires 36 bytes (normals, texture coords, coords)
      1 Million polygons
      36 Mb/s only for geometry
      60 fps -> 2080 Mb/s throughput between processor and graphics hardware.
      Textures can take up Giga bytes of data
      Animation data etc...
  We need special hardware for an efficient handling of this.
    Upload geometry/textures once.

## Slide 16
Before GPUs
  Specialized solutions
  Very expensive
  Small market
SGI Octane
Intergraph Wildcat 500 80Mb AGP

## Slide 17
1st Generation GPUs
  Fixed function only (No shaders)
  Performance (TNT2)
    150 MHz
  230 Million pixels/second
  2.4 GB/s memory bandwidth
ATI Rage2
NVIDIA TNT2

## Slide 18
2nd Generation
  First ‘GPU’* (Geforce256)
  Still fixed function (no shaders)
  Added H/W T&L (Transform and Lighting), cube mapping, and bump mapping
* "a single-chip processor with integrated transform, lighting, triangle setup/clipping, and rendering engines that is capable of processing a minimum of 10 million polygons per second.” per NVIDIA
Nvidia Geforce 256
ATI Radeon 7500

## Slide 19
3rd Generation
  Programmable Vertex shaders
  No programmability for Pixel shaders
Nvidia Geforce 3
ATI Radeon 8500
XBOX

## Slide 20
4th Generation Cards
  Pixel Shaders
  Loops and Branches in Vertex shaders (not in Pixel shaders)
Nvidia GeForce FX 5650
Nvidia GeForce FX 5650

## Slide 21
5th Generation Cards
  Loops and Branches also in Pixel Shaders
  Multiple Render Targets (MRT)
Nvidia GeForce 6800
ATI Radeon X800

## Slide 22
6th/7th Generation
  Geometry Shaders
  Tessellation Shaders
Nvidia GeForce 8800
ATI Radeon X1600

## Slide 23
8th Generation
State of the Art
  Real-time Ray Tracing
    NVIDIA GeForce RTX 2080 Ti
    AMD/ATI Radeon 5700 XT

## Slide 24
Specs – Old vs New
  OLD (~2005)
    Intel 3 Ghz
      12 GFLOPS peak (via SSE2)
    NVIDIA GeForce 6800
      45 GFLOPS peak performance
  More recent
    Intel Core i9-7900X
      10 cores @ 3.3GHz (4.3GHz max)
      1.15 TFLOPS
    NVIDIA GeForce RTX 2080 Ti
      2944 Cores @ 1.55GHz
      13.45 TFLOPS

## Slide 25
Fillrate development
Data from wikipedia
350000
300000
250000
200000
150000
100000
50000
0
Fill rate MT/S

## Slide 26
How GPUs are FAST!
  What’s really important these days is parallelism, massive parallelism
    Superscalar processing
    NVIDIA GeForce RTX 2080 Ti – 2944 Cores

## Slide 27
Parallelization of rendering
  Divide work into sub-tasks
  Sorting schemas:
    Sort-first
    Sort-middle
    Sort-last fragment
    Sort-last image
A
SORT
G G G
FG
FG
FG
FM
FM
FM
DISPLAY
A – Application
G – Geometry stage
FG – Fragment generator
FM – Fragment merging

## Slide 28
Sort-first
  Sort primitives before geometry processing
  Divide screen into tiles
  Each process work on a tile in parallel, merge result
    Good use for multiscreen-tiled displays
    Used in SLI configurations
  Disadvantage: pre-transform are required
A
SORT
G G G
FG
FG
FG
FM
FM
FM
DISPLAY
A – Application
G – Geometry stage
FG – Fragment generator
FM – Fragment merging

## Slide 29
Sort-middle
  Geometry processors are given work arbitrary—load balancing is the goal
  Each rasterizer (FG+FM) is given a tile (part of display, scanline, group of pixels etc.)
  Transformed primitives is then sorted into corresponding rasterizer
    Multiple rasterizers can get same primitive
A
SORT
G G G
FG
FG FG
FM
FM
FM
DISPLAY
A – Application
G – Geometry stage
FG – Fragment generator
FM – Fragment merging

## Slide 30
Sort-middle (con’t)
  Used in most mobile GPUs
    Minimize bandwidth requirement.
      Need system memory support.
      High memory bandwidth usage will hammer the whole system.
    Save more penguins (power).
      Reducing memory access means less power consumption.
  Disadvantage
    One triangle may go into multiple tiles.
    Need a sorting buffer after triangle sorting
      More complex scene, more memory access.
    Completely divide graphic pipeline into two partition.
      This may harm the performance.
A
SORT
G G G
FG
FG FG
FM
FM
FM
DISPLAY
A – Application
G – Geometry stage
FG – Fragment generator
FM – Fragment merging

## Slide 31
Sort-last fragment
  Sort fragments after FG before FM
  Primitives distributed evenly over geometry units (G)
  Fragment are generated, and then sorted into Fragment-merge (FM)
  Imbalance can occur if a set of large triangles are sent to one FG
  Used in original XBox
A
G G G
FG
FG
FG
FM
FM
FM
DISPLAY
SORT
A – Application
G – Geometry stage
FG – Fragment generator
FM – Fragment merging

## Slide 32
Sort-last image
  Primitives split over separate pipelines, balancing
  Complete rendering to z-depth
  Final composite into image using depth.
G G G
FG
FG
FG
FM
FM
FM
DISPLAY
A
A – Application
G – Geometry stage
FG – Fragment generator
FM – Fragment merging

## Slide 33
Sort-last image (con’t)
  Used in most desktop GPUs
    Minimize performance issue
      Sorting cost is low
    Desktop GPU has its own dedicated memory.
      Graphics DRAM usually has high bandwidth with high latency.
  Advantage
    Full rendering pipeline without interrupt until per-fragment operation (compare to sort-middle)
  Disadvantage
    Large amount of data to be sent
    Huge bandwidth requirement on frame buffer access, particularly in high resolution and anti-aliasing enable.
G G G
FG
FG
FG
FM
FM
FM
DISPLAY
A
A – Application
G – Geometry stage
FG – Fragment generator
FM – Fragment merging

## Slide 34
Busses: Feed the beast
PCI based—one bus shared by all traffic including GPU
AGP Based—Dedicated bus for the graphics cards
PCI express—latest generation of dedicated bus

## Slide 35
Busses
  PCI, 1993
    33MHz/32-bit PCI bus
    The whole bus can deliver: 133MB/second
    Usually peaks at: 100-110MB/sec
  AGP 1.0, 1996
    1x, 2x – 250MB/second; 32Bit
    Runs in full memory bus speed
  AGP 2.0, 1998
    4x – 266.67MHz, (4 x 66 MHz), 1066MB/second
  AGP 3.0, 2002
    8x – 533MHz, 2.1GB/Sec
  PCI-Express, 2003
    16x – 4GB/sec in each direction
    Doesn’t share BW with other PCI-Express slots
  PCI-Express 6.0, 2021
    16x – 126GB/sec

## Slide 36
Additional busses
  NVIDIA SLI
    Hooking up two or more cards so that they can work in parallel.
    Drivers distribute workload between the cards
    For example
      GPU 0 renders frame 0, 2, 4, 6…
      GPU 1 renders frame 1, 3, 5, 7…

## Slide 37
Know your architecture
    Optimal performance is usually tied to one platform
    Knowing the target platform is very important

## Slide 38
The Graphics Pipeline
  We could look at the 3D rendering application as a pipeline
    Compare to a factory assembly
    The stages operate in parallel but are stalled until all stages are done
    We cannot execute faster than the slowest stage which is called the bottleneck
    The rendering process is conceptually built like a pipeline

## Slide 39
The Graphics Pipeline
Application
Geometry
Rasterizer

## Slide 40
The Graphics Pipeline
  Data will be pushed through the stages of the pipeline
  The slowest stage will determine the rendering speed, expressed in frames per second.
  Each stage can be further parallelized
    Compare to description of NVIDIA hardware

## Slide 41
Application stage
  User have full control over this stage as it is executed in software
    Input – User interaction, Simulations
    Output – Object transform, View transform, rendering primitives
  Reads input on
    From devices
    From the user
    From the Network
  The simulation that drives the application
    Physics, AI, collision detection, animation
  Performance affected by
    Complexity of simulation, simulation size (Number of objects)
    Reading from slow devices, network etc...

## Slide 42
Geometry stage
  Performance affected by
    Number of lights, geometry complexity, shader complexity, effect complexity, etc.
  Find bottleneck by using a profiler and/or disabling various components
Model & View Transform
Lightning
Projection
Clipping
Screen
Mapping

## Slide 43
Rasterizer
  Output
    Pixels in frame buffer
  Performance affected by
    Size of window
    Number of/size of textures
  Find the bottleneck by
    Increase the window size, if performance drops -> fill limited application

## Slide 44
Optimization
  Extreme Programming
    Simple design, implement fast, test often, if need redesign, but test first!
  Optimizing code is a hard task, but don’t over-optimize
  Locate the major bottlenecks, remove them, move on

## Slide 45
Optimizing
  The bottleneck can move between the different pipeline stages.
  Example, assume:
    Application stage: 30ms
    Geometry stage: 20ms
    Rasterizer: 40ms
  The maximum framerate is then 1/40ms=25Hz
  Optimizing the application stage won’t improve framerate!
    Although, we could use the extra time at the geometry stage (20ms idle time) for doing more complex lighting equations

## Slide 46
Optimizing
  Some stages are hard to test individually, as they are implemented in specialized hardware.
  What we have to do is to setup a number of tests, where each test only affects one stage at a time.

## Slide 47
Testing Application stage
  Usually executed on CPU
  If CPU ~100% we could be CPU limited
  Locate the problem
    Use profiling tools
      CodeAnalyst (AMD)
      VTune Analyzer (INTEL)
    Send down data that causes the other stages to do little or no work, if CPU still 100%, the problem is in the Application stage

## Slide 48
Testing geometry
  Add/remove lights
  Try different kinds of lights
    Directional less computational intensive
    Point lights
    Spotlights - most demanding
  If performance changes, we are transform-limited
  If we are using programmable shaders, we can remove the lighting equation, to see if performance increases.

## Slide 49
Testing Rasterizer
  Size of rendered surface
  Turn off blending and depth buffering

## Slide 50
Overall optimization
  Reduce the number of primitives
    Culling (later on)
    Reduce the complexity of the models
    Level of detail—render object only as accurate as necessary
  Choose as low a precision as is possible
    Vertices, normals, texture coordinates (watch out for anomalies!)
  Turn of features not used
    Fog, blending, lighting, transparency etc..
  Preprocess the models
    Most hw prefers triangles and quads, not polygons (>4 corners)
    Tri-strips reduces data sent over the bus